## Slide 1
A Topology-Aware Framework for
Intra-Urban Transport
Policy Targeting
Dhaka, Bangladesh
A Four-Version Comparative Analysis of Road Network Topology Clustering
Mehzad Galib | Md. Sabbir Hossain
Bangladesh University of Engineering and Technology (BUET) · February 2026
V1
1km/Drive
V2
1km/All
V3
Data-Driven
V4
2km Grid

## Slide 2
Dhaka — Why This City Matters
22M+
Metropolitan Population
25 km/km²
Peak Road Density
400 Years
Layered Urban History
5 distinct
Historical Morphological Logics
The Challenge
Dhaka grew through 400 years of largely unplanned organic densification punctuated by discontinuous RAJUK planned interventions. Standard Western archetype frameworks (Maze / Grid / Radial / Periphery) assume morphologically segregated zones — something Dhaka fundamentally does not have.
Five Morphological Logics
River-Radial — Roads radiating from Buriganga ghats Moghul Organic — Dense goli lane networks, bazaar spines RAJUK Sector Grid — Post-1947 planned residential zones Ribbon Corridor — Linear development along arterials Informal Infill — Ad-hoc densification of agricultural plots

## Slide 3
Original Research Proposal
Can unsupervised graph clustering reveal discrete morphological archetypes in Dhaka's road network?
01
OSM Extract
network_type='drive'
bbox: 23.65–23.85°N
02
1km Grid
800m buffer per cell
03
23 Features
Topology per subgraph
04
PCA
95% variance retained
05
K-Means
Silhouette/CH selection
06
Label
Maze / Grid / Radial / Periphery
Expected outcome: k = 4 clusters mapping to the four archetype types, validated against known Dhaka neighbourhoods.

## Slide 4
Four Key Methodological Deviations from the Proposal
Network Type
Was:
drive only
→
Now:
all roads (footpaths, lanes, service roads)
Why: drive excluded Old Dhaka's goli lanes — clustering measured OSM coverage, not topology
Bounding Box
Was:
north = 23.85°N
→
Now:
north = 23.95°N (Uttara, Diabari included)
Why: Truncated bbox removed the clearest planned Grid zones from the dataset entirely
Feature Set
Was:
23 features, reciprocity, raw path
→
Now:
27 features — Gini fixed, entropy, normalised
Why: Gini formula gave negative values; reciprocity saturated at 0.98 across all zones
Labelling
Was:
Archetypes imposed by formula score
→
Now:
V3–V4: data-driven neutral Cluster_0/1 labels
Why: Archetype scoring forced Western typologies onto patterns unique to South Asian cities

## Slide 5
27 Topological Features — Three Functional Groups
Structural Topology (V1 baseline)
density
transitivity
avg_clustering_coef
avg_degree
n_scc / n_wcc
gscc_pct / gwcc_pct
path_length_p90
V2 Corrections & Additions
orientation_entropy ← replaces reciprocity
wcc_fragmentation ← periphery detector
hub_dominance_ratio ← radial detector
path_length_p90_norm ← size corrected
betweenness_gini ← formula fixed
mean_strength_norm ← normalised
Centrality Features (LCC-scoped)
mean_in/out_degree_centrality
mean_closeness_centrality
mean_betweenness_centrality
mean_katz_centrality
mean_pagerank
global_efficiency
local_efficiency
★ Features that consistently discriminated across all 4 versions: global_efficiency · gwcc_pct · wcc_fragmentation · betweenness_gini

## Slide 6
Version 1: Baseline — 1 km Grid / Drive Network / Imposed Archetypes
469
zones analysed
k = 2
best cluster count
0.366
silhouette score
57 / 43
Maze / Grid split %
What the clusters showed
Metric
Maze
Grid
Node count (mean)
719
77
Global efficiency
0.088
0.238
gwcc_pct
93.2%
82.7%
Closeness centrality
0.056
0.165
Confidence score
0.761
0.709
⚠ Critical Diagnosis
The 9.3× node count gap (Grid: 77, Maze: 719) is inverted from what urban morphology predicts.
Old Dhaka should have MORE nodes than Uttara — not fewer. The inversion occurred because
network_type='drive' excluded Old Dhaka's goli lanes while capturing all of Uttara's grid streets.
The algorithm measured
OSM coverage anisotropy by road classification — not urban topology. The feature heatmap was perfectly binary: a single size confound dominated all 23 features.

## Slide 7
Version 2: All-Roads Network + Corrected Features — Imposed Labels
821
zones (+75% vs V1)
k = 2
best cluster count
0.420
silhouette (↑ +0.054)
79 / 21
Maze / Grid split %
What Improved
✓ 75% more zones — organic network fully captured ✓ Silhouette improved 0.366 → 0.420 ✓ Gini formula corrected (was negative — now 0–1) ✓ wcc_fragmentation clearly separates clusters (0.021 vs 0.109) ✓ global_efficiency gap widened: 0.116 vs 0.303
⚠ What Still Failed
✗ orientation_entropy failed to discriminate: Grid 3.502 vs Maze 3.557 — gap of only 0.055 Dhaka's lake perimeters force curved roads in planned zones too ✗ hub_dominance_ratio nearly identical (1.676 vs 1.620) No radial archetype detected ✗ DBSCAN collapsed to 1 cluster — no density-based separation 'Grid' cluster = peripheral fragmented zones, not planned grids

## Slide 8
Version 3: Data-Driven Labels — Removing Western Archetypes
827
zones (≈ V2)
k = 2
best cluster count
0.408
silhouette (≈ V2)
78 / 22
Cluster_1 / Cluster_0 %
Cluster Profiles
Feature
Cluster_0
Cluster_1
Zone count
184 (22%)
643 (78%)
global_efficiency
0.286
0.108
gwcc_pct
75.9%
92.7%
wcc_fragmentation
0.099
0.020
betweenness_gini
0.574
0.675
orientation_entropy
3.560
3.580 ← identical
Key Finding from V3
Removing Western archetype labels produced zero change in cluster structure. The k=2 result is not an artefact of the labelling system — it is a genuine property of Dhaka's road network in feature space. Cluster_0 (22%) = Peripheral fragmented zones Low gwcc_pct (75.9%), high wcc_fragmentation — incomplete road infrastructure at the city edge Cluster_1 (78%) = Dense connected urban core High gwcc_pct (92.7%), high betweenness Gini — few critical junctions carry most of the network flow

## Slide 9
Version 4: Scale Experiment — 2 km Grid / Best Silhouette / Extreme Split
226
zones (↓ from 827)
k = 2
best cluster count
0.551
silhouette (best ever)
91 / 9
Cluster_0 / Cluster_1 %
2km Cluster Profiles
Feature
Cluster_0
Cluster_1
Zones
206 (91%)
20 (9%)
node_count (mean)
1,264
83.8
gwcc_pct
93.6%
61.4%
global_efficiency
0.079
0.255
betweenness_gini
0.716
0.596
orientation_entropy
3.700
3.650 ← still no gap
Interpretation
Best silhouette (0.551) but most extreme split (91/9). At 2 km scale, every cell is large enough to average planned + organic layers — the same problem that affected 1 km cells at the block scale now repeats at the neighbourhood scale. The PCA scatter shows Cluster_0 as a dense compact cloud while the 20 peripheral zones (Cluster_1) are widely dispersed — confirming the minority cluster is heterogeneous rather than a coherent type. orientation_entropy again shows near-zero discriminating power across all 226 zones.

## Slide 10
Comparative Results — Silhouette Scores & Cluster Splits
Chart: KMeans Silhouette Score (k=2) by Version
| V1 (1km/drive/imposed) | V2 (1km/all/imposed) | V3 (1km/all/data-driven) | V4 (2km/all/data-driven)
Silhouette at k=2 | 0.366 | 0.42 | 0.408 | 0.551
Chart: Cluster Split % by Version
| V1 | V2 | V3 | V4
Majority | 57 | 79 | 78 | 91
Minority | 43 | 21 | 22 | 9

## Slide 11
Feature Discrimination — What Works vs. What Fails
Feature
V1 Gap
V2 Gap
V3 Gap
V4 Gap
Discriminates?
global_efficiency
0.150
0.187
0.178
0.176
STRONG
gwcc_pct
10.5%
18.5%
16.8%
32.2%
STRONG
wcc_fragmentation
N/A
0.088
0.079
0.075
MODERATE
betweenness_gini
N/A
0.099
0.101
0.120
MODERATE
density
0.034
0.044
0.041
0.026
MODERATE
hub_dominance_ratio
N/A
0.056
0.075
0.152
WEAK
orientation_entropy
N/A
0.055
0.020
0.050
FAILS
reciprocity (V1)
~0
Removed
—
—
FAILS

## Slide 12
The Core Finding
Dhaka Exhibits a
Connectivity Spectrum —
Not Discrete Archetypes
k = 2 in all 4 versions
Consistent across every network type, feature set, and labelling strategy — multi-criteria confirmed by Silhouette AND Calinski-Harabasz
k = 4 silhouette 25–35% below k = 2
Every version penalises the proposed four-cluster structure. The expected archetype solution is statistically rejected.
DBSCAN: 1 cluster, 4 versions
No density-based separation in feature space — the data forms a continuous distribution, not discrete clumps
The two clusters that
DO exist are real:
High-connectivity dense core
(78–91% of zones)
Low-connectivity peripheral fringe
(9–22% of zones)

## Slide 13
Why Dhaka Resists Classification — Literature Grounding
Porta et al. (2006)
Bologna, Barcelona, Venice — primal graph archetypes work in cities with segregated morphological zones
Boeing (2019)
Orientation entropy effective for grid vs. organic in 100 cities — but tested on cities without lake-perimeter curvature effects
Revi et al. (2011)
South Asian megacity networks are historical palimpsests — planned fragments embedded in organic fabric at every scale → continuous gradient, not zones
Taubenböck et al. (2017)
Delhi's morphology cannot be meaningfully classified by Western archetypes below ward level — 500m grid works, 100–200m does not
Islam (2005)
Dhaka: five interleaved morphological logics, none spatially segregated — planned and organic coexist in the same 1km cell at every location in the city

## Slide 14
Alternative Classification Approaches
Spectral Clustering
Operates on zone-similarity graph — detects non-convex, elongated clusters K-Means cannot find. May reveal finer structure in Dhaka's continuous PCA manifold.
Note: Difficulty setting kernel bandwidth without ground truth labels
Hierarchical Agglomerative (HAC)
Builds a dendrogram showing cluster hierarchy at all levels simultaneously. Reveals whether data supports k=2, then k=4, or remains flat.
Note: Computational cost for 827+ zones with full linkage
Self-Organising Maps (SOM)
Projects 27D feature space onto 2D grid preserving topology. If Dhaka's zones form a connected manifold (confirmed continuous spectrum) vs. islands (discrete types).
Note: Fleischmann et al. (2021) — used for urban morphology gradients
RAJUK Supervised Classification
Reframe as supervised: use RAJUK land-use zones as ground truth. Does topology predict planning intent? Answerable question with clear null hypothesis.
Note: Recommended next step — converts discovery problem to validation problem
Thana-Level Analysis
Administrative boundaries more closely follow historical morphological zones than a regular grid. Requires distributed graph processing (cuGraph/GraphX) for 50k–300k node subgraphs.
Note: Computationally infeasible with NetworkX in-memory — needs GPU infrastructure

## Slide 15
Limitations
OSM Data Completeness
Peripheral zones had completeness ratios below 0.3 — up to 70% of road network absent. Clustering in these zones reflects data sparsity as much as genuine topology. Barrington-Leigh & Millard-Ball (2017): Bangladesh OSM ~83% complete overall, but urban core coverage >> rural.
1 km Scale Mismatch
Grid sits between Dhaka's two meaningful morphological scales — micro blocks (100–300m) and neighbourhoods (3–5km). Every 1km cell contains a similar mixture of planned skeleton + organic infill, making all zones statistically similar.
Orientation Entropy Failure
Feature fails in Dhaka due to lake-perimeter curvature (Dhanmondi) creating artificial high entropy in planned zones, and informal lane networks following slow-varying parcel edges producing moderate (not high) entropy.
Thana-Level Infeasibility
Thana subgraphs at all-roads level: 50,000–300,000 nodes. NetworkX O(n²/n³) scaling made computation > 45 min per thana. Requires Apache Spark GraphX or NVIDIA cuGraph (GPU) infrastructure.
Single-City Scope
Results specific to Dhaka. Cities with more uniform planning history (Chandigarh, Islamabad) may cluster cleanly. Cities with even greater complexity (Kolkata, Mumbai) may show weaker clustering still.

## Slide 16
Conclusion
What Four Versions Proved
The Methodology Journey IS the Result
V1→V4 did not fail to cluster Dhaka — it demonstrated that Dhaka resists the clustering framework. Each version corrected a real failure and the k=2 result survived every correction. Resistance is empirically meaningful.
The Two Clusters Are Actionable
High-connectivity dense core vs. low-connectivity peripheral fringe — geographically stable across all versions. Low-connectivity zones (9–22%) are where infrastructure investment has highest network-wide impact.
Recommended Next Step
Supervised classification using RAJUK land-use zones as ground truth. Reframes: 'discover archetypes?' → 'does topology predict planning intent?' A tractable, answerable research question.
Mehzad Galib | Md. Sabbir Hossain · BUET · February 2026